Plan Revision Memo

Date:               12 October 2022

# From:             Hopwood, Ryan J.

National Product Development - Architecture

Ryan.Hopwood@mdch.com

720-977-3642

Plan #’s:         D769 – Boston_D770 - Chicago

Subdivisions:  Haskins Station

Rev. No.:        D769/D770-007

The Following Revisions have been made:

On Plan D769 of the D769/D770 duplex, the party wall behind the kitchen cabinets was changed from a 2x4 wall to a 2x6 wall to provide adequate space to run the range hood vent up through the wall. By adding an additional 2” to this wall, the Closet and Pantry front wall and the mechanical soffit above also get pulled forward 2”.

- Sheets – Sheet A0.0a – Title Sheet

- Plan Revision added

- Sheet A1.1a – First Floor Plan

- 2x4 party wall behind the kitchen cabinets changed to a 2x6 wall.

- Front wall of the Closet and Pantry moves out 2”.

- Mechanical soffit above moves out 2”

- Sheet A5.1a – First Floor Flooring Breaks

- Kitchen sq. ft changed per wall update.

- Sheet E1.1a – First Floor Electrical Plan

- Outlets at kitchen counter and range moved out 2” per wall update.